## Slide 1
Teledyne Detector Update
Presented by James W. Beletic
10. October 2013
Selmer Anglin1, James Beletic1, Richard Blank1, Craig Cabelli1, Scott Cabelli1, Jing Chen1, Richard Demers1, Mark Farris1, Don Lee1, Gerard Luppino2, Anders Petersen1, Eric Piquette1, Andre Wong1, and Min Xu1
1 Teledyne Imaging Sensors, 5212 Verdugo Way, Camarillo, CA 93012, USA
2 GL Scientific, 3367 Waialae Avenue, Honolulu, HI 96816, USA
Scientific Detector Workshop 2013
7-11 October
Florence, Italy

## Slide 2
2
Space & Astronomy
Market Segment
Instrumentation
Engineered Systems
Digital Imaging
Aerospace and
Defense Electronics
Dedicated to the Scientific Community
2

## Slide 3
DLR Offner Spectrometer
Image Sensor
BAE Fairchild
Backside illuminated CMOS
1024×128 pixels
24×24 µm pixel size
1 Me- full well
70 e- noise (high gain)
13 bit column parallel ADC
Copy of EnMAP VNIR spectrometer
420-1000 nm
5 nm spectral sampling

## Slide 4: High-Performance Image Sensor Technologies
Three Key Technologies
Growth and processing of HgCdTe detector
Design and fabrication of CMOS readout circuit
Hybridization of detector to CMOS readout
The highest performance
infrared sensors are
Hybrid CMOS image sensors.
H1R/H1RG
1024x1024 pixels
HST WFC3
WISE
OCO
Deep Impact/EPOXI
OSIRIS-REx
H4RG-15
4096x4096 pixels
Ground-based astronomy
Future NASA missions
HST ACS
LDCM TIRS
JWST
OSIRIS-REx
Euclid
WFIRST
Explorer Missions
SIDECAR ASIC
Focal Plane Electronics
H4RG-10
4096x4096 pixels
JMAPS
OPTIIX
HST SM5
WFIRST
H2RG
2048x2048 pixels
JWST
Euclid
Ground-based astronomy
WFIRST
  Moon Mineralogy Mapper
  Mars Reconnaissance Orbiter (CRISM)
  Artemis
  AVIRIS
  PRISM
  HyspIRI
  Comet Hopper
640x480 pixels
1280x480 pixels
1600x480 array in development
Developments for NASA Missions
Long-wave infrared sensors for NEOCam asteroid survey mission
Sparse readout soft x-ray sensor
HyspIRI Visible-SWIR and HyspIRI Thermal IR (30-kHz frame rate)
H4RG-10 IR for WFIRST
FINESSE Exoplanet Prototype
Imaging Spectroscopy Sensors
4

## Slide 5
II
III
IV
V
VI
Detector Families
Si - IV semiconductor
HgCdTe - II-VI semiconductor
InGaAs & InSb - III-V semiconductors
InAs + GaSb - III-V Type 2
Strained Layer Superlattice (SLS)
5

## Slide 6
Tunable Wavelength: Unique property of HgCdTe
Hg1-xCdxTe Modify ratio of Mercury and Cadmium to “tune” the bandgap energy
G. L. Hansen, J. L. Schmidt, T. N. Casselman, J. Appl. Phys. 53(10), 1982, p. 7099
λco = 5.3 mm
HgCdTe crystal is grown by MBE on CdZnTe Substrates
6

## Slide 7: Growth Structure of p-on-n HgCdTe arrays
7

## Slide 8: High-Performance Sensors Serving Space Astronomy
Array sizes: 128x128 to 4096x4096 pixels
High-quantum efficiency (>80%)
Low readout noise (<6 electrons)
Focal plane electronics
Space flight packaging
Supporting NASA Explorer, New Frontiers, Discovery mission developments
NICMOS, WFC3, ACS Repair
NIRCam, NIRSpec, FGS
Bands 1 & 2
Lander (çiva)
IR spectrograph
IR spectrograph
HST
JWST
New Horizons
Deep Impact
& EPOXI
Rosetta
JMAPS
4Kx4K Arrays & Electronics
WFIRST
WISE
Euclid
IR spectrograph
OSIRIS-REx
CRISM (Vis & IR)
Mars
Reconnaissance
Orbiter
8

## Slide 9
Initial Technology Development
2002 2003 2004 2005 2006 2007 2008 2009 2010 2011 2012
Product Phase 1
Product Phase 2
H2RG Visible - IR Array Performance and Reliability
Process Improvement
Substrate Removal
Higher quantum efficiency in IR
Visible response (with high QE)
Less susceptible to cosmic rays
Eliminates fringing in the substrate
Reliability Improvement
Improved Balanced Composite
Structure (BCS)
Process Improvements
Lower dark current
Eliminate dark current tail
Higher operability
Higher yields
Dark Current
Lowered mean
Eliminated tail
Process Improvement
Lower interpixel capacitance
Process Improvement
Lower readout noise
Process Improvement
Reduced Persistence
Improved UV hard “blue” QE
Reliability Improvement
Bake stability & storability
H2RG Product Improvements: 2002 - 2013
9

## Slide 10: Performance Confirmed by Users
Data: Courtesy of ESO, KMOS project
Record noise performance:
Fowler-32 noise < 2.5 electrons
Readout Noise [e-rms]
0
2
4
6
8
Number of Fowler Pairs
0
1,000
10
100
10,000
Quantum efficiency (QE) greater than 80% from visible to IR (shown for 2.5 micron cutoff device)
0.0
0.2
1.0
1.2
Quantum Efficiency
0.4
0.6
0.8
Number of Pixel
Wavelength [micron]
1.0
2.5
1.5
2.0
Mean correlated double sampling (CDS) noise on 3 Science Grade and Engineering Grade KMOS FPAs below 10 electrons
Readout Noise [e-rms]
0
30
10
20
40
0.0
0.5e5
2.0e5
2.5e5
1.0e5
1.5e5
10

## Slide 11
2002 2003 2004 2005 2006 2007 2008 2009 2010 2011 2012
Vertical Integration
Cryogenic SCA Package
Quasi kinematic mechanical mount
High flatness and parallelism
Comprehensive electrical interface
Mosaic Focal Plane Arrays
2x2 Mosaic modules
Scientific Instruments
Camera systems
Cryogenic foreoptics
Optics calibration modules
HxRG Integration
photons in
analog voltages out
SIDECAR ASIC Focal Plane Electronics
Ultra-compact cryogenic focal plane electronics on a chip
Room-temperature interface electronics
Cable
photons in
digital signal out
Training, Integration & Installation
Camera Systems
Stirling Cooler Cryostat
Lab instrumentation
photons in
FITS files out
SIDECAR ASIC Software & Integration Team
Software solutions
Dedicated customer interfaces
11

## Slide 12: H4RG-15 Focal Plane Development
200 mm Silicon CMOS wafer with four
H4RG-15 ROIC die
H4RG-15 dummy hybrid array on SiC with SIDECAR ASIC in next-generation package
Kicked off at Teledyne in December 2009
First prototype arrays have been fabricated and tested
On-sky evaluation in May - July 2012
Pilot production starting in March 2013
Whirlpool Galaxy, ULBCam, May 2012
4096×4096, 15 µm pixel pitch FPA
Significantly reduces price / pixel
Maintain established H2RG performance
Project funded by US National Science Foundation
12

## Slide 13: Teledyne makes visible sensors also: H4RG-10 HyViSI
4096×4096 pixels
10 micron pixel pitch
Silicon Hybrid CMOS on SiC pkg
Challenges:
  Charge Diffusion Crosstalk
  Interpixel Coupling Crosstalk
  Readout noise
13

## Slide 14: 10 µm cutoff for NEOCam asteroid survey mission
Image Sensor Requirements | 
Wavelength (µm) | 6 – 10
Operating temperature range (K) | 35 – 40
Integration time (s) | 10
Dark current (e-/s/pixel) | <200
Read noise (correlated double sample; e-) | <30
Quantum efficiency (%) | >60
Well depth (e-) | >45,000
Pixel operability (%) (with all above properties) | >90
McMurtry et al., Optical Engineering 52, 091804 (2013)
McMurty et al
SDW2013 Presentation
Friday, 11 Oct .
14

## Slide 15: SIDECAR ASIC – Focal Plane Electronics on a Chip
SIDECAR ASIC
36 analog input channels
36 16-bit ADCs: up to 500 kHz
36 12-bit ADCs: up to 10 MHz
20 output bias channels
32 digital I/O channels
Microcontroller (low power)
LVDS or CMOS interface
Low power:
<15 mW, 4 channels, 100 kHz, 16-bit ADC
<150 mW, 32 channels, 100 kHz, 16-bit ADC
Operating temperature: 30K to 300K
Interfaces directly to H1RG, H2RG, H4RG
Qualified to NASA TRL-9
  Vibration, radiation, thermal cycling
  Radiation hard to ~100 krad
JWST SIDECAR ASIC package
Hubble Space Telescope
SIDECAR ASIC package
(Hermetically Sealed)
SIDECAR ASIC
Ground-based package
Cryogenic SIDECAR Package (Hermetically Sealed)
SIDECAR ASIC cryogenic focal plane electronics with H2RG FPA
15

## Slide 16: The new SIDECAR Module (SMd)
The SMd supports
  32 outputs (64 outputs in dual SMd configuration)
  Buffered and unbuffered operation of all Teledyne’s HxRG SCAs (x = 1, 2, and 4)
  Slow mode (up to 500 kpix/sec/port, 16 bit A/D)
  Fast mode (up to 5 Mpix/sec/port, 12 bit A/D); up to 10 Mpix/sec/port, 32 output dual SMd configurations)
Operating temperature: 77 K – 323 K
Mass: <100 g
16

## Slide 17: SMd Configurations and Performance
Selmer Anglin et al SDW2013 Poster Friday, 11 Oct.
4×4 H2RG mosaic + 16 SMd
64 Megapixel IR
Focal Plane Array for Euclid
SMd-s (“s” for space qualified)
Manufactured, screened, and qualified for direct use in space flight applications
Passive components screened to EEE-INST-002, level 1
SMd-e (“e” for engineering model)
Manufactured to the same print as the SMd-s
Passive components are only “space qualifiable”, i.e. they are the same components as in the SMd-s, but have not been screened to EEE-INST-002
SMd-g (“g” for ground-based)
Manufactured to the same print as the SMd-s
Passive components are commercial off the shelf (COTS) components, not appropriate for space flight
17
1 2 4 8 16 32 64
Sample Size
Readout Noise (e-)
0 2 4 6 8 10
H2RG w/ SMd Readout Noise
  CDS 8.5 e-
  Fowler16 2.5 e-
  Fowler64 1.5 e-
Scott Cabelli et al Poster Thu. 10. Oct.

## Slide 18: H2RG – SIDECAR ASIC Fast Mode Performance
18
Mark Farris et al SDW 2013 Poster Friday, 11 Oct.
Temperature | 250mV | 500mV | 1000mV
130K | 57 e- | 71 e- | 53 e-
150K | 70 e- | 68 e- | 50 e-
10 Mpix/sec/port
32 outputs
66 Hz full frame rate
GBA H2RG SMd SAM

## Slide 20: Hybrid CMOS Imaging Sensors
Readout Circuit
Input signal
  Flux – object and background
Operating Mode
  Integration time
  Frame readout time
  Shutter (rolling, snapshot)
  Multiple storage cells per pixel
  Windows
  Reset (pixel, line, global)
  Event driven
Interface
  Input (analog, digital)
  Output (analog, digital)
  # of readout ports
Environment
  Temperature
  Radiation
Other Requirements
  Linearity
  Anti-blooming
The functionality (“the brains”) of a CMOS-based sensor is provided by the readout circuit
Detector
Wavelength (λ)
Quantum Efficiency
Dark current & Noise
Radiation environment
Persistence
20

## Slide 21: Pixel Amplifier Options
21

## Slide 22
CHROMA™ - Product for Hyperspectral Applications
30 µm pixel pitch, CTIA design
Snapshot, integrate-while-read (IWR) operation
Correlated Double Sampling (CDS) in pixel for noise reduction
Maximum full frame rate of 125 Hz
  Configurable window by rows for faster frame reads
  Frame rate is inversely proportional to number of rows read out
Dynamic range of 9000:1 (ratio of full well size to noise)
Stitched in format multiples of 160 columns by 480 rows
Rick Demers et al SDW 2013 Poster Wednesday, 9 Oct.
CHROMA 1280×480 pixel array
22

## Slide 23
GeoSnap™ - 2K×2K Pixel CTIA Product
For Low to Moderate Flux Applications
The 2048×2048 pixel GeoSnap™ is a state-of-the-art CTIA readout integrated circuit (ROIC) for visible and infrared low to moderate flux scientific applications
Compatible with Teledyne’s HgCdTe infrared (IR) and silicon PIN HyViSI™ visible detectors
Digital input and digital output (ADCs on-chip)
23

## Slide 24
Teledyne Imaging Sensors
Everywhereyoulook™
THANK YOU FOR YOUR ATTENTION