## Slide 1
Large Format Array developments at Sofradir and CEA for Science and Astronomy applications

## Slide 2
  30 years of heritage on Infrared detectors design and manufacture, mainly for HgCdTe technology
  800 people, >100 people dedicated to space applications
  80 Flight Models delivered over the past decade ; 18 already in space, 20+ planned for launch in 2017-2018
  Contractor of most of European space missions with IR imaging (Meteosat Third Generation, Sentinel satellites, METimage, 3MI, ExoMars)
Sofradir in a few words

## Slide 3
  The objective of the studies is to answer European Space Agency (ESA) needs for their Cosmic Vision program (2015-2025) including science and astronomy applications
  What ESA needs :
    SWIR Large Format Arrays (LFA)
    Products made by an European manufacturer
    Components capable of working in low fluxes environments
  These activities were initially competitive between Leonardo/UKATC and CEA-LETI/CEA-IRFU/Sofradir (technologies development)
  The current phase has been contracted with Sofradir only
Context of the studies

## Slide 4
  ESA expected missions
    ARIEL : detection of exoplanetary systems ; large FPA imaging detector, pitch ≥ 15µm, 2 channels in MWIR and LWIR wavelengths
    THESEUS : exploration of the Early Universe by unveiling the faintest GRBs population ; NIR spectrometer
    Future missions to come…
  ESO ELT instruments
    HARMONI : spectrograph made of 4 channels of 8k x 4k pixels, pitch ≥ 15µm, Visible / SWIR wavelengths
    MICADO : diffraction limited imager, mosaic of 12k x 12k, pitch ≥ 15µm, SWIR wavelengths
    METIS : 4k x 4k spectrograph mosaic + 2kx2k imaging detector, pitch ≥ 15µm, MWIR wavelengths
    Future instruments to come…
  Others ? Contact us !
Potential Applications

## Slide 5
Capability of our technologies to meet the specifications
  Specifications
  Detector under test definition
    Detection Circuit main characteristics
    Readout Circuit design
  Detector under test performances
Detector size scale up
  ALFA detector requirements
  Scale up capability
  Development schedule
  Astronomy projects roadmap
Scope of the presentation

## Slide 6
Capability of our technologies to meet the specifications
Capability of our technologies to meet the specifications
Detector size scale up

## Slide 7
Specifications
Parameter | Requirement
Cut-on wavelength | ≤ 0.8 µm
Cut-off wavelength | < 2.3 µm
Quantum efficiency | ≥ 70%
Operating temperature | ≥ 100K
Dark current (at 100K) | ≤ 0.1 e-/pix/s
Linear well capacity | ≥ 60 ke-
Non-Linearity | ≤ 3%
Cross-talk | ≤ 2%
Readout noise (single CDS) | ≤ 18 e- rms
Readout speed | ≥ 100 kHz

## Slide 8
  Component tested in the previous LFA development studies
  HgCdTe material hybridized component
  Format :
    640x512 pixels
    15 µm pitch
SWIR LFA detector under test definition

## Slide 9
  Epitaxy type : both MBE and LPE have been studied
  Diodes technology :
    p on n technology (more than 10 years of experience for CEA-LETI and Sofradir teams)  better QE is expected compared to n on p technology
  Wavelength range:
    0.8µm cut-on (non removed CdZnTe substrate)
    2.1µm / 2.3µm cut-off
Detection Circuit main characteristics

## Slide 10
  Source Follower per Detector : Integration on the PV diode capacitance
Readout Circuit design
  Capabilities :
    Unitary diode reset
    Readout through follower MOS
    Non-destructive reading
  Advantages:
    High impedance
    Well adapted for low fluxes
    Low readout noise
Unbuffered output
Buffered output
Column
Pixel
Output buffer
Reset
Line select
Column select
Sub PV

## Slide 11
  Quantum efficiency measured by ESA :
    ~75% for LPE epitaxy components
    ~60% for MBE epitaxy components
  Dynamic range
    Diode capacitance :15fF to 20fF
  Non linearity
    ~3.2% for LPE components
    ~2.5% for MBE components
  Readout Noise
    11.4 e- to 11.5 e- on test pixels
  Cross-talk
    0.6% for LPE components
    1.1% for MBE components
Detector performances
LPE
MBE
2500
2000
1000
500
1500

## Slide 12
  Dark Current at 100K : measurement is hardly achievable because of glow effect due to the ROIC
Detector performances
Nominal Ouput node bias
Minimum Ouput node bias
0.5 e-/s
  It has been performed by reducing bias level : minimum dark current measured is 0.5e-/s
  We still need to work on glow reduction to reach lower measurements

## Slide 13
Performances summary
Parameter | Requirement | Value | Compliancy
Operating wavelength | 0.9 – 2.0µm | 0.8- 2.1µm | 
Cutoff wavelength | <2.3µm | 2.1µm | 
Quantum efficiency | ≥70% | 74% mean value | 
Operating temperature | ≥100K | 100K | 
Dark current (at 100K) | ≤0.1 e-/pix/s | <0.5e-/s | 
Linear well capacity | ≥60ke- | 60ke- | 
Non-Linearity | ≤3% | 3.2% and 2.5% | 
Cross-talk | ≤2% | 0.6% to 1.1% | 
Readout noise (single CDS) | ≤18e- rms | 11.4 to 11.5e- | 
Readout speed | ≥100kHz | 100kHz | 
ROIC glow hides dark current

## Slide 14
Detector size scale up
Capability of our technologies to meet the specifications
Detector size scale up

## Slide 15
ALFA detector requirements
Parameter | Value
Array size - pitch | 2048x2048 – 15µm
Spectral range | Cut-on ≤ 0.8µm, cut-off 2.1µm / 2.5µm
Operating temperature | 100 ± 1 K
Quantum efficiency | ≥ 70%
Dark current (at 100K) | ≤ 0.1 e-/pix/s
Linear well capacity | ≥ 60ke-
Non linearity | ≤ 3%
Cross talk (inter pixel capacitance / other contributions) | ≤ 2% / ≤ 3%
Readout noise (single CDS) | ≤ 18e- rms
Readout speed | ≥ 100kHz

## Slide 16
ALFA program : NIR detector development
2048x2048 Hybridized Circuit – 15µm NIR/SWIR
30 years heritage in HgCdTe IR detectors manufacturing
LETI : 50 years heritage in HgCdTe technology
Detection circuit development
ROIC design
Hybridization and Packaging
IRFU : 40 years in developing and testing instrumentation for space missions
Component EO characterizations
  Astronomy Large Focal plane Array
  ESA program + Labex FOCUS (french labs) fundings
  French consortium
Involved in ESO METIS instrument

## Slide 17
Asteroid program : manufacturing means
  ASTronomy EuROpean Infrared Detector
  European consortium (H2020 program contracted with European Commission)
  Main goal : to develop the technology that will make Europe non-dependent for large IR detectors compatible with large volume production
  Use of larger CdZnTe wafers
    From current 2.5 inches size (1 Detection Circuit) to 3.5 (4 DC)
    First batch already manufactured
3.5’’ vs 2.5’’

## Slide 18
  2048x2048 pixels matrix, composed by:
    2042x2042 sensitive pixels
    A ring of reference pixels : fixed capacitance
    1 row of specific reference pixels : different capacitance values
    1 row of test pixels : ROIC functionality, pixel leakage, parasitic capacitance…
  ROIC capabilities
    Windowing capability
    Readout modes : rolling shutter, non-destructive readout
    Readout frequency : 100 kHz (Science mode)
    6MHz (Fast mode)
    1, 4 or 32 output
  Packaging designed with 4 sides buttability for mosaic imaging
ALFA detector design

## Slide 19
  Prototyping : hybridization of 4 NGP matrix (1024x1024) on a single test vehicle
  Total size of the prototype ~40% larger than the size of the LFA under development
  Number of good connections after hybridization > 99.9% of pixels
Multi Cross sections on 2 axis  99.999% rate of interconnection
A block of 4 CMOS readout 1024x1024 - NGP
Equivalent 2428x2428 15µm pitch detector
Hybridization capability

## Slide 20
Nov.
Feb.
May
Aug.
Nov.
2018
Today
02/2019
TRR
09/2018
CDR
11/2017
KO
11/2016
Tasks 5 : Detectors Characterization
Task 4 : Detectors manufacturing and sorting
Task 3 : Detailed Detector Design
Tasks 1&2 : Review of requirements, Preliminary Design, Test Plan Preparation
2017
2016
PDR
02/2017
Feb.
May
Aug.
Nov.
Feb.
May
Aug.
2019
Project end
ALFA development schedule

## Slide 21
Astronomy projects roadmap
Already Available
On going
To come…
  MCT p/n technology with low dark current and high QE
  SFD input stage ROIC with low noise capability
  Technologies scale up (ROIC and MCT) up to 2Kx2K format keeping the EO performances
  Hybridization capability demonstration on 2Kx2K size FPA
  Packaging development for mosaic imaging
  Large volume production capability
  Potential development of 2k² MWIR detection circuit (5.3µm cut-off)
  ESA development of a FPA controller (ASIC) in order to have a full European-made system (FPA + controller)
2016
2018

## Slide 22
  Sofradir / CEA technologies are meeting astronomy requirements
  The device scale up is on-going, using existing validated technologies
  The new European-made 2Kx2K 15µm pitch detector (ALFA) will be available in Q1/2019
  Large volume production capability is addressed through Asteroid program
Conclusion

## Slide 23
Thank you !