## Slide 1: University Astronomy
Professor Don Figer
Instruments and Detectors I

## Slide 2: Aims for Lecture
Introduce modern Optical/NIR/UV instrumentation.
  instrument requirements
  instrument examples
Describe capabilities of commonly used instruments.
  HST
  Spitzer
  Chandra
  JWST
  ELTs
  WFIRST

## Slide 3: instrument requirements

## Slide 4: Instrument Science Requirements
spatial resolution
spectral resolution
wavelength coverage
sensitivity
dynamic range
field of view

## Slide 5: Instrument System Requirements
spectrograph and/or camera
sampling
filters
exposure time cadence (short/long)
stability
  photometric
  spectral

## Slide 6: Instrument Engineering Requirements
detector/electronics
  pixel size
  quantum efficiency
  noise
  dark current
  supported exposure times
  sampling speed
optics
  materials
  irregularity/wavefront error
  f/number
  optics efficiency
  coatings
mechanics
environment
  pressure
  temperature
  stability

## Slide 7: Instrument Constraints
cost
schedule
volume
mass
power

## Slide 8
red=optics
blue=rays
black=focal/pupil planes
green=optical axis
primary
collimator
camera
prime focal plane
pupil plane
final focal plane
FT
Fcoll
Fcam
qT
scam
sT
Camera plate scale

## Slide 9: Camera f/number, seeing-limited
In general, we want to ensure Nyquist sampling, so the camera f/number should be chosen such that two pixels span the FWHM of the point spread function (PSF).
If the PSF is fixed by seeing, then the size would be roughly equal for all telescope sizes.
Therefore, bigger telescopes (bigger D) will require smaller camera f/numbers in order to maintain the same plate scale.
Consider a seeing-limited 8m telescope with 10 mm pixels, fcam~1.

## Slide 10: Camera f/number, diffraction-limited
Consider a diffraction-limited telescope.
Now, fcam is independent of telescope size.
Consider, 10 mm pixels in optical light, fcam~30.

## Slide 11: instrument components

## Slide 12: Optics: example

## Slide 13: Electronics
There are many kinds of electronics in an instrument.
Detector
  control
    clock
    bias
  data acquisition
    readout multiplexer
    pre-amplifier
    digitizer
Motion control
Thermometry
Computer(s)

## Slide 14: Electronics: example
Astronomical Research Cameras, Inc. (Bob Leach)
8 channels per board
1 MHz, 16-bit A/D
Clocks
Biases
Voodoo/OWL software

## Slide 15: Focal Plane Assembly
The FPA contains the detector(s) and provisions for optical, mechanical, thermal, and electrical interfaces.

## Slide 16: Focal Plane Assembly: example

## Slide 17: Mechanics: Telescope Interfacing

## Slide 18: Software
data acquisition
control
virtual instrument
quick look
quick pipeline
data reduction pipeline
simulators

## Slide 19: instrument examples - existing

## Slide 20: NIRSPEC/Keck Optical Layout Side View

## Slide 21: NIRSPEC/Keck Optical Layout Top View

## Slide 22: Hubble Space Telescope Cutaway

## Slide 23: Hubble Space Telescope Field of View
WFC3
ACS
STIS
COS
FGS

## Slide 24: HST: WFC3

## Slide 25: HST: WFC3

## Slide 26: HST: ACS

## Slide 27: HST: ACS

## Slide 28: Chandra Space Telescope
ACIS
HRC
Spectral modes
Advanced Charged Couple Imaging Spectrometer (ACIS): Ten CCD chips in 2 arrays provide imaging and spectroscopy; imaging resolution is 0.5 arcsec over the energy range 0.2 - 10 keV; sensitivity: 4x10-15 ergs/cm2/sec in 105 s
High Resolution Camera (HRC): Uses large field-of-view mircro-channel plates to make X-ray images: ang. resolution < 0.5 arcsec over field-of-view 31x31 arc0min; time resolution: 16 micro-sec sensitivity: 4x10-15 ergs/cm2/sec in 105 s
High Energy Transmission Grating (HETG): To be inserted into focused X-ray beam; provides spectral resolution of 60-1000 over energy range 0.4 - 10 keV
Low Energy Transmission Grating (LETG): To be inserted into focused X-ray beam; provides spectral resolution of 40-2000 over the energy range 0.09 - 3 keV

## Slide 29: Chandra Space Telescope: ACIS

## Slide 30: Chandra Space Telescope: HRC

## Slide 31: Chandra Space Telescope: Spectroscopy
High Resolution Spectrometers - HETGS and LETGS
These are transmision gratings
  low energy: 0.08 to 2 keV
  high energy: 0.4 to 10 keV (high and medium resolution)
Groove spacings are a few hundred nm.

## Slide 32: Gemini (North)

## Slide 33: Gemini (South)

## Slide 34: instrument examples - future

## Slide 35: JWST
NIRCAM
NIRSPEC
MIRI

## Slide 36: JWST: NIRCAM
Nyquist-sampled imaging at 2 and 4 microns -- short wavelength sampling is 0.032"/pixel and long wavelength sampling is 0.065"/pixel
2.2'x4.4' FOV for one wavelength provided by two identical imaging modules, two wavelength regions are observable simultaneously via dichroic beam splitters.

## Slide 37: JWST: NIRSPEC
1-5 um; R=100, 1000, 3000
3.4x3.4 arcminute field
Uses a MEMS shutter for the slit

## Slide 38: JWST: MIRI
5-27 micron, imager and medium resolution spectrograph (MRS)
MIRI imager: broad and narrow-band imaging, phase-mask coronagraphy, Lyot coronagraphy, and prism low-resolution (R ~ 100) slit spectroscopy from 5 to 10 micron.
MIRI will use a single 1024 x 1024 pixels Si:As sensor chip assembly. The imager will be diffraction limited at 7 microns with a pixel scale of ~0.11 arcsec and a field of view of 79 x 113 arcsec.
MRS: simultaneous spectral and spatial data using four integral field units, implemented as four simultaneous fields of view, ranging from 3.7 x 3.7 arcsec to 7.7 x 7.7 arcsec with increasing wavelength, with pixel sizes ranging from 0.2 to 0.65 arcsec. The spectroscopy has a resolution of R~3000 over the 5-27 micron wavelength range. The spectrograph uses two 1024 x 1024 pixels Si:As sensor chip assemblies.

## Slide 39: JWST: MIRI MRS

## Slide 40: TMT
The Wide Field Optical Spectrometer (WFOS) will provide near-ultraviolet and optical (0.3 – 1.0 μm wavelength) imaging and spectroscopy over a more than 40 square arcminute field-of-view. Using precision cut focal plane masks, WFOS will enable long-slit observations of single objects as well as short-slit observations of hundreds of objects simultaneously. WFOS will use natural (uncorrected) seeing images.
The Infrared Imaging Spectrometer (IRIS) will be mounted on the observatory MCAO system and be capable of diffraction-limited imaging and integral-field spectroscopy at near-infrared wavelengths (0.8 – 2.5 μm).
The Infrared Multi-object Spectrometer (IRMS) will allow close to diffraction-limited imaging and slit spectroscopy over a 2 arcminute diameter field-of-view at near-infrared wavelengths (0.8 – 2.5 μm).

## Slide 41: GMT

## Slide 42: E-ELT
Two first-light instruments have been identified: a diffraction-limited near-infrared imager (ELT-CAM) and a single-field near-infrared wide-band integral field spectrograph (ELT-IFU), including the adaptive optics systems required to deliver their science cases.
The next three instruments, a mid-infrared imager and spectrometer (ELT-MIDIR), a high resolution spectrometer (ELT-HIRES) and a multi-object spectrometer (ELT-MOS), were considered of equal scientific importance.
Fabrication is underway with the consortia that will build ELT-IFU (HARMONI), ELT-CAM (MICADO), the MCAO system (MAORY) and ELT-MIDIR (METIS).

## Slide 43: WFIRST-AFTA Observatory Concept
Key Features
Telescope: 2.4m aperture primary
Instruments
  Wide Field Imager/Spectrometer & Integral Field Unit
  Internal Coronagraph with Integral Field Spectrometer
Overall Dry Mass: ~4060 kg (CBE)
Structure: high stiffness composites; modular packaging for avionics
GN&C/Propulsion: inertial pointing, 3-axis stabilized, mono-prop system for stationkeeping & momentum unloading
Data Downlink Rate: Continuous ~600 Mbps Ka-band to dedicated ground station
C&DH: low rate bus for housekeeping and spacecraft control, high speed bus for science data
Power: ~2400 W average power (CBE)
GEO orbit
Launch Vehicle: Delta IV Heavy
GSFC: leads mission, wide field instrument, spacecraft
JPL: leads telescope, coronagraph

## Slide 44: WFIRST-AFTA Field Layout

## Slide 45: Wide Field Instrument Overview
Key Features
Wide field channel instrument for both imaging and spectroscopy
  3 mirrors, 1 powered
  18 4k x 4k HgCdTe detectors cover 0.76 - 2.0 mm
  0.11 arc-sec plate scale
  Single element wheel for filters and grism
  Grism used for GRS survey covers 1.35 – 1.89 mm with R = 461l (~620 – 870)
IFU channel for SNe spectra, single HgCdTe detector covers 0.6 – 2.0 mm with R between 80-120
Focal Plane Assembly
Optical Bench
Cold Electronics
Cold Optics Radiation Shield
Element Wheel
Notes: Telescope & wide field channel optical design is coaxial
  Reduced fabrication and alignment risk by simplifying optics in instrument (tertiary mirror is a conic instead of anamorphic)
  Field of view is arced rather than a rectangular array of 6x3 H4RG-10s; enables favorable optical interface to coronagraph
IFU is repackaged, similar elements in a much smaller overall volume
  Simplifies integration by enabling parallel build and integration with wide field channel
Grism assembly simplified; all fused silica, 3 elements, with simpler surfaces; 2 instead of previous 1 diffractive surface
Cryocooler
  Detector operating temperature reduced from 120K to 100K based on recent detector testing – lower temperature necessary to meet WFIRST requirements.
  Low jitter Turbo Brayton cooler allows colder operational temperatures than can be achieved passively in GEO orbit while minimizing jitter.

## Slide 46: WFI Filters

## Slide 47: Coronagraph Instrument Overview
Temperature | 293 K for instrument
Temperature | ~165 K for cameras
Data Volume | ~30 Gbits/day
Imaging | 0.43 – 0.97 microns, 4.8" FoV 0.009" pixel scale, 1K×1K EMCCD
Integral Field Spectrograph | 0.60 – 0.97 microns R~70